## Slide 1: Integrated Visual Landing Aid Sensor
PSU Capstone 2019

## Slide 2: OBJECTIVES
Select an affordable quadcopter & autopilot for demonstration
Integrate 1500-OEM with autopilot
Create a custom board or harness for easy integration
Demonstrate safe landing from a fixed height
Create documentation / tutorials

## Slide 3: Landing Aid
Large outer pattern allows detection from large distance
As platform gets closer, algorithm switches to inner pattern
  Reverse contrast
Pattern is known to software ahead of time
  constantly “looking”
  no training needed
Target center is returned as pixel coordinates (row, column)
Specific pattern geometry allows calculation of angle of rotation (degrees)
Geometry of pattern also allows calculation of distance to target
  Small target = farther away, Larger target = closer
  Requires knowledge of lens Field of View (FoV)
All of which gets translated into controls to autopilot

## Slide 4: Hardware
???

## Slide 5: Hardware
How to power 1500 & camera
  4.5 to 5.5V DC
  2 - 3 Watts with camera, etc.
  connectors & cables
  Battery life
How to communicate with autopilot
  RS-232 or 3.3VTTL
  Optional: i2c not recommended
How to mount to aircraft
  Weight
  Physical position
    Balanced, clear of obstacles, etc.
  Mechanical coupling and enclosure - nuts and bolts kind of things
Camera selection
  SightLine camera
Operational Height vs Lens selection
  See Lens / FoV calculator

## Slide 6: Hardware Goals
Phase 0 - Pick a Platform
Pixhawk quad-copter or similar
Suitable for indoor & outdoor use
Find a “kit”
Phase 1 - Simple cable harness
1500-OEM to Pixhawk - Power and communication
Quick prototype - allow software to be tested, understand aircraft control, etc.
Everything else is already available
Phase 2 - Build a camera board
Combine 1500-FPC and sensor reference design into a single board
  Serial Connector (3-pin molex) to Pixhawk
  Power connector (2 or 4-pin molex) from batter or Pixhawk
  Digital video connector (50-pin Hirose)
    Parallel digital video
    i2c sensor control
    Power
    3.3V TTL serial
  Mounting for lens
Phase 3 - Mechanical: Find, design, or otherwise build a simple enclosure

## Slide 7: Mockup
Digital Video
Power
Serial
Command and Control
Power
Pixhawk

## Slide 8: Camera Sensor
AR0134 ON Semiconductor Monochrome Image Sensors
  1280 x 960 (1.2 MPixels)
  Monochrome
  -30° to 80°C
Evaluation Board here
  Schematics etc should all be available
SightLine already works with 3rd party board built on same image sensor
  Reduces software need for sensor command and control (should “just work”)

## Slide 9: Software
???

## Slide 10: Communication

## Slide 11: Software Goals
Phase 0 - Become familiar with basic quadcopter control (Mission Planner?)
Phase 1 - Compile and install SightLine Sample
SightLine has sample code ready to deploy on our hardware
Verify serial comms to Pixhawk are functional
Understand outputs and how they relate to Phase 0
Phase 2 - Tuning
Experiment with landing pattern and output to determine how they affect the gains used to control the quadcopter
Modify existing sample code to read in parameters for tuning
Phase 3 - Dynamic Tuning
Create / Utilize a command and control interface for tuning parameters at runtime

## Slide 12: Software - Mission Planner
Used to configure and control the aircraft
Can a custom “widget” be created to configure the software running on 1500?